## Slide 1: Always on capacity exchange (AOCE)
Conceptual introduction/Strawman Proposal
December 16, 2020
Reliable Energy Analytics LLC

## Slide 2: What is an aoce (pronounced ace)
An online, 24x7, Marketplace for Sellers and Buyers to transact in both Capacity and Energy contracts (i.e. a PPA), operated by Independent System Operators (ISO), modeled on the REBA and Level Ten Marketplaces
A platform for ISO’s to secure capacity for reliability that honors individual State based energy targets and eliminates the cost of acquiring excess capacity, that is occurring today
A more flexible platform for acquiring the right amount of capacity, closer to when it’s needed, as opposed to the 3-year planning horizon used by some ISO’s today, while also supporting long term new capacity projects
An approach that anticipates, and accommodates, daily increases in new supply coming from behind the meter resources and other distributed energy resources
A new, dynamic marketplace that properly values Green Capacity/Energy and other characteristics/services that may be valuable for reliability, i.e. rapid ramping
A place where anyone: Generators, Energy Suppliers, Traders, Investors, Utility Companies, State’s, Companies with their own Green agenda, and of course, ISO’s, can buy and sell capacity, on their own terms i.e. duration, type, location, price
A market mechanism that achieves just and reasonable price points for all stakeholders

## Slide 3: AOCE Objectives
Ensure that we have a reliable electrical system for all, at a just and reasonable price point for all stakeholders
Achieve State Energy as a top priority, that properly charges the beneficiaries of that State, without burdening other States consumers with costs of the program
Be market based so that each resource is properly valued for the services it provides to grid operations, consumers, the environment and society at large
Efficiently secures future capacity using a just-in-time approach that eliminates the excessive over-buying of capacity that occurs today by ISO’s while supporting new, long term capacity construction projects
Incentivizes investment in the most beneficial technologies used to generate electricity and manage grid operations reliably (including DR) that achieves Societal and Environmental goals determined by each individual State, such as clean air and water
Provide a vibrant. 24x7, marketplace for Investors and Green Energy Buyers to secure PPA’s and Investors to trade

## Slide 4: AOCE Conceptual design; Capacity Commitments
Capacity Sellers
receive qualification
approval from their
local ISO to place
offers in AOCE
Buyers place bids
in AOCE to secure capacity
and/or Energy
Capacity Sellers
place offers in AOCE,
backed by a qualified
Resource
Aligned Bids/Offers
Result in a
Capacity Commitment (CC)
ISO approved
CC results in an
Approved Capacity Commitment (ACC)
CC Buyers become
the Owners of ACC’s
ISO controlling the
Locations in the
Bid/Offer must
Approve a CC for
feasibility

## Slide 5: Capacity Supply Obligations from ACC’s
The ISO performs the CSO Issuance
Process (CSOIP) for resources
located within ACC’s resulting in CSO’s to
Capacity Resource Owners of an ACC,
establishing a Uniform Clearing Price per
grid service (CSOIP Step 2) or as part of each
States clearing Process (CSOIP Step 1)
CSO
Capacity Resource Owner
ACC
Some Resource Owners
in an ACC may not
receive a CSO due to
reliability concerns.
ACC owners receive
no capacity payment
in this case
Owners (Buyers) of ACC’s receive capacity payments equal to the uniform clearing price multiplied by the Amount of MW’s in the CSO Issued to generators in an ACC

## Slide 6: CSO Issuance Process (CSOIP)
Market Rules determine when this process is executed
The ISO will prioritize the issuance of CSO’s for ACC’s as follows:
  Satisfy State based energy targets using a cost curve and uniform clearing price, like DA Energy Market, based on State provided parameters.
  Satisfy Reliability Requirements by issuing a CSO to ACC resources based on a priority services hierarchy (see Note below) specified by Market Rules, using a cost curve and uniform clearing price, like the DA Energy Market, to properly compensate Generators and Investors for their commitment
  The ISO may refuse to issue a CSO to an ACC resource, based on reliability concerns
  In the event that an ISO is unable to secure enough capacity to meet reliability requirements, via this process, one or more ISO Reliability Bid’s (ISORB) may be placed into the AOCE to secure required capacity
  NOTE: A priority services hierarchy instructs an ISO on the type and quantity of grid services to be acquired in precedence order, using a fuel and technology neutral approach, to meet reliability requirements.

## Slide 7: ISO Reliability targets and Bids
At some point the ISO calculates the Reliability Target MW’s (ISORT)
for a specific Commitment Period and Location
Total Amount of Reliability MW needed for a location and timeframe (commitment period), determined by ISO
MINUS
CSO’s already issued for the same
location and Commitment Period
time frame, determined
by ISO
ISO Reliability Target (ISORT)
indicating additional MW’s
that are needed by an ISO to
satisfy Reliability Requirements
ISO submits one or more
Reliability Bids (ISORB)
into AOCE, specifying
ISORT MW, Capacity type,
location and other
characteristics

## Slide 8: CSO Issuance Process for Offers to ISORB’s
The ISO for a Control Area
performs a CSO Issuance
Process (CSOIP)
resulting in CSO’s to Capacity
Resource/ACC Owners based on
their submitted offers to the ISORB’s
in AOCE
The ISO only awards enough CSO’s to
satisfy the calculated ISORT
No excess MW above ISORT
may be acquired
CSO
Capacity Resource Owner
OR
ACC Owner
of submitted/cleared
offers
Capacity payments are made by the ISO
To ACC/Capacity Owners of cleared
Offers that are issued a CSO. No
profit/uplift payment is made. Payment
Is based on MW * Price
Submitted Offers to ISORB
ACC Owners with no CSO and
Capacity Resource Owners with
Available capacity may
submit Offers to
satisfy an ISORB

## Slide 9: Energy Markets, PPA’s and Energy Payments
An ACC that specifies an
Energy Revenue Percentage > 0
Is a Power Purchase Agreement
Capacity Resource Owners with Capacity
Supply Obligations MUST submit Energy offers
into the Energy Markets.
ISO performs SCUC/SCED the same
as today’s DA/RT Energy Markets
Generators produce
Energy throughout the
Operating day, some
may be self-scheduled
ISO processes Settlements to
determine payments for Energy
and compensates the appropriate
party

## Slide 10: Capacity Charges to cover Capacity Payments
Capacity Charges are issued to Load
Serving Entities throughout a control
area for all capacity payments
made by an ISO servicing that area.
Capacity Charges are allocated to
LSE’s, based on the location specified
in the (ACC/ISORB) Bids
Bids that apply to the entire
control area location will have their
Capacity Charges allocated to
LSE’s based on a fair and appropriate
allocation scheme,
i.e. proportion or nominal
load in the region
This Photo by Unknown Author is licensed under CC BY-SA-NC